## Slide 1
Introduction to DHT11: Temperature and Humidity Sensor
The DHT11 is a versatile and affordable temperature and humidity sensor widely used in various applications. Understanding its workings can enable efficient monitoring of environmental conditions in diverse contexts.
by swaraj upgrad

## Slide 2
DHT11 Specifications and Features
Temperature
Range: 0°C to 50°C
Accuracy: ±2°C
Humidity
Range: 20% to 90% RH
Accuracy: ±5% RH
Other
Voltage: 3.5V to 5.5V
Sampling Rate: 1 Hz

## Slide 3
DHT11 Internal Structure
Humidity Sensor
Capacitive humidity sensor
Temperature Sensor
NTC Thermistor
Integrated Circuit
Converts analog to digital
Single-wire Communication
Serial data transmission

## Slide 4
Working Principle: Humidity Sensing
Capacitance change
Humidity levels affect sensor's capacitance
Digital Conversion
Internal IC converts capacitance into a digital value
Oscillator Measurement
IC uses an oscillator to measure the capacitance

## Slide 5
Working Principle: Temperature Sensing
1
Resistance Change
NTC thermistor's resistance varies with temperature
2
Voltage Divider Circuit
IC measures resistance using a voltage divider
3
Digital Conversion
IC converts voltage into a digital temperature value

## Slide 6
DHT11 Data Transmission Protocol
Start Signal
MCU initializes communication
Response Signal
DHT11 confirms readiness
Data Transmission
40-bit data packet sent serially
Bit Transmission
Each bit encoded with pulse duration

## Slide 7
Applications of DHT11
Home Weather Stations
Monitoring indoor temperature and humidity
Agricultural Monitoring
Measuring environmental conditions
HVAC Systems
Controlling temperature and humidity
Data Loggers
Recording temperature and humidity data

## Slide 8
Limitations and Alternatives
1
Limited temperature and humidity range
2
Lower accuracy than more expensive sensors
3
Slower sampling rate
4
Susceptible to noise and interference